## Slide 1
Parallelization

## Slide 2: Outline
Why Parallelism
Parallel Execution
Parallelizing Compilers
Dependence Analysis
Increasing Parallelization Opportunities

## Slide 3: Moore’s Law
8086
286
386
486
Pentium
P2
P3
P4
Itanium
Itanium 2
From David Patterson
1,000,000,000
100,000
10,000
1,000,000
10,000,000
100,000,000
From Hennessy and Patterson, Computer Architecture: A Quantitative Approach, 4th edition, 2006
Number of Transistors

## Slide 4: Uniprocessor Performance (SPECint)
8086
286
386
486
Pentium
P2
P3
P4
Itanium
Itanium 2
From David Patterson
1,000,000,000
100,000
10,000
1,000,000
10,000,000
100,000,000
From Hennessy and Patterson, Computer Architecture: A Quantitative Approach, 4th edition, 2006
Number of Transistors

## Slide 5: Multicores Are Here!
1985
1990
1980
1970
1975
1995
2000
4004
8008
8086
8080
286
386
486
Pentium
P2
P3
P4
Itanium
Itanium 2
2005
20??
# of
cores
1
2
4
8
16
32
64
128
256
512
Athlon
Raw
Power4
Opteron
Power6
Niagara
Yonah
PExtreme
Tanglewood
Cell
Intel
Tflops
Xbox360
Cavium
Octeon
Raza
XLR
PA-8800
Cisco
CSR-1
Picochip
PC102
Boardcom 1480
Opteron 4P
Xeon MP
Ambric
AM2045
Notes: Lets look at a simplified graph of showing a log scale of the number of cores for some commodity microprocessors versus their date of introduction.
For 35 years, uniprocessor designs dominated the commodity microprocessor market.
But their end has come due to the limited scalability of their global, monolithic structures.
The major cpu vendors have stopped development of uniprocessor designs.
In the last 5 years, commodity processor designers have turned to multicore designs to continue performance scalability.
From 2 cores up to hundreds of cores.

## Slide 6: Issues with Parallelism
Amdhal’s Law
  Any computation can be analyzed in terms of a portion that must be executed sequentially, Ts, and a portion that can be executed in parallel, Tp. Then for n processors:
  T(n) = Ts + Tp/n
  T() = Ts, thus maximum speedup (Ts + Tp) /Ts
Load Balancing
  The work is distributed among processors so that all processors are kept busy when parallel task is executed.
Granularity
  The size of the parallel regions between synchronizations or the ratio of computation (useful work) to communication (overhead).

## Slide 7: Outline
Why Parallelism
Parallel Execution
Parallelizing Compilers
Dependence Analysis
Increasing Parallelization Opportunities

## Slide 8: Types of Parallelism
Instruction Level Parallelism (ILP)
Task Level Parallelism (TLP)
Loop Level Parallelism (LLP) or Data Parallelism
Pipeline Parallelism
Divide and Conquer Parallelism
 Scheduling and Hardware
 Mainly by hand
 Hand or Compiler Generated
 Hardware or Streaming
 Recursive functions

## Slide 9: Why Loops?
90% of the execution time in 10% of the code
  Mostly in loops
If parallel, can get good performance
  Load balancing
Relatively easy to analyze

## Slide 10: Programmer Defined Parallel Loop
FORALL
  No “loop carried dependences”
  Fully parallel
FORACROSS
  Some “loop carried dependences”

## Slide 11: Parallel Execution
Example
  FORPAR I = 0 to N
  A[I] = A[I] + 1
Block Distribution: Program gets mapped into
  Iters = ceiling(N/NUMPROC);
  FOR P = 0 to NUMPROC-1
  FOR I = P*Iters to MIN((P+1)*Iters, N)
  A[I] = A[I] + 1
SPMD (Single Program, Multiple Data) Code
  If(myPid == 0) {
  …
  Iters = ceiling(N/NUMPROC);
  }
  Barrier();
  FOR I = myPid*Iters to MIN((myPid+1)*Iters, N)
  A[I] = A[I] + 1
  Barrier();

## Slide 12: Parallel Execution
Example
  FORPAR I = 0 to N
  A[I] = A[I] + 1
Block Distribution: Program gets mapped into
  Iters = ceiling(N/NUMPROC);
  FOR P = 0 to NUMPROC-1
  FOR I = P*Iters to MIN((P+1)*Iters, N)
  A[I] = A[I] + 1
Code fork a function
  Iters = ceiling(N/NUMPROC);
  FOR P = 0 to NUMPROC – 1 { ParallelExecute(func1, P); }
  BARRIER(NUMPROC);
  void func1(integer myPid)
  {
  FOR I = myPid*Iters to MIN((myPid+1)*Iters, N)
  A[I] = A[I] + 1
  }

## Slide 13: Parallel Execution
SPMD
  Need to get all the processors to execute the control flow
    Extra synchronization overhead or redundant computation on all processors or both
  Stack: Private or Shared?
Fork
  Local variables not visible within the function
    Either make the variables used/defined in the loop body global or pass and return them as arguments
    Function call overhead

## Slide 14: Parallel Thread Basics
Create separate threads
  Create an OS thread
    (hopefully) it will be run on a separate core
  pthread_create(&thr, NULL, &entry_point, NULL)
  Overhead in thread creation
    Create a separate stack
    Get the OS to allocate a thread
Thread pool
  Create all the threads (= num cores) at the beginning
  Keep N-1 idling on a barrier, while sequential execution
  Get them to run parallel code by each executing a function
  Back to the barrier when parallel region is done

## Slide 15: Outline
Why Parallelism
Parallel Execution
Parallelizing Compilers
Dependence Analysis
Increasing Parallelization Opportunities

## Slide 16: Parallelizing Compilers
Finding FORALL Loops out of FOR loops
Examples
  FOR I = 0 to 5
  A[I] = A[I] + 1
  FOR I = 0 to 5
  A[I] = A[I+6] + 1
  For I = 0 to 5
  A[2*I] = A[2*I + 1] + 1

## Slide 17: Iteration Space
N deep loops  N-dimensional discrete iteration space
  Normalized loops: assume step size = 1
FOR I = 0 to 6
FOR J = I to 7
Iterations are represented as coordinates in iteration space
  i̅ = [i1, i2, i3,…, in]
0 1 2 3 4 5 6 7  J
0
1
2
3
4
5
6
I 

## Slide 18: Iteration Space
N deep loops  N-dimensional discrete iteration space
  Normalized loops: assume step size = 1
FOR I = 0 to 6
FOR J = I to 7
Iterations are represented as coordinates in iteration space
Sequential execution order of iterations  Lexicographic order [0,0], [0,1], [0,2], …, [0,6], [0,7], [1,1], [1,2], …, [1,6], [1,7], [2,2], …, [2,6], [2,7], ……… [6,6], [6,7],
0 1 2 3 4 5 6 7  J
0
1
2
3
4
5
6
I 

## Slide 19: Iteration Space
N deep loops  N-dimensional discrete iteration space
  Normalized loops: assume step size = 1
FOR I = 0 to 6
FOR J = I to 7
Iterations are represented as coordinates in iteration space
Sequential execution order of iterations  Lexicographic order
Iteration i̅ is lexicograpically less than j̅ , i̅ < j̅ iff there exists c s.t. i1 = j1, i2 = j2,… ic-1 = jc-1 and ic < jc
0 1 2 3 4 5 6 7  J
0
1
2
3
4
5
6
I 

## Slide 20: Iteration Space
N deep loops  N-dimensional discrete iteration space
  Normalized loops: assume step size = 1
FOR I = 0 to 6
FOR J = I to 7
An affine loop nest
  Loop bounds are integer linear functions of constants, loop constant variables and outer loop indexes
  Array accesses are integer linear functions of constants, loop constant variables and loop indexes
0 1 2 3 4 5 6 7  J
0
1
2
3
4
5
6
I 

## Slide 21: Iteration Space
N deep loops  N-dimensional discrete iteration space
  Normalized loops: assume step size = 1
FOR I = 0 to 6
FOR J = I to 7
Affine loop nest  Iteration space as a set of linear inequalities
  0 ≤ I
  I ≤ 6
  I ≤ J
  J ≤ 7
0 1 2 3 4 5 6 7  J
0
1
2
3
4
5
6
I 

## Slide 22: Data Space
M dimensional arrays  M-dimensional discrete cartesian space
  a hypercube
Integer A(10)
Float B(5, 6)
0 1 2 3 4 5
0
1
2
3
4
0 1 2 3 4 5 6 7 8 9

## Slide 23: Dependences
True dependence
  a =
  = a
Anti dependence
  = a
  a =
Output dependence
  a =
  a =
Definition: Data dependence exists for a dynamic instance i and j iff
  either i or j is a write operation
  i and j refer to the same variable
  i executes before j
How about array accesses within loops?

## Slide 24: Outline
Why Parallelism
Parallel Execution
Parallelizing Compilers
Dependence Analysis
Increasing Parallelization Opportunities

## Slide 25: Array Accesses in a loop
  FOR I = 0 to 5
  A[I] = A[I] + 1
0 1 2 3 4 5 6 7 8 9 10 11 12
0 1 2 3 4 5
Iteration Space
Data Space

## Slide 26: Array Accesses in a loop
  FOR I = 0 to 5
  A[I] = A[I] + 1
0 1 2 3 4 5 6 7 8 9 10 11 12
0 1 2 3 4 5
Iteration Space
Data Space
= A[I]
A[I]
= A[I]
A[I]
= A[I]
A[I]
= A[I]
A[I]
= A[I]
A[I]
= A[I]
A[I]

## Slide 27: Array Accesses in a loop
  FOR I = 0 to 5
  A[I+1] = A[I] + 1
0 1 2 3 4 5 6 7 8 9 10 11 12
0 1 2 3 4 5
Iteration Space
Data Space
= A[I]
A[I+1]
= A[I]
A[I+1]
= A[I]
A[I+1]
= A[I]
A[I+1]
= A[I]
A[I+1]
= A[I]
A[I+1]

## Slide 28: Array Accesses in a loop
  FOR I = 0 to 5
  A[I] = A[I+2] + 1
0 1 2 3 4 5 6 7 8 9 10 11 12
0 1 2 3 4 5
Iteration Space
Data Space
= A[I+2]
A[I]
= A[I+2]
A[I]
= A[I+2]
A[I]
= A[I+2]
A[I]
= A[I+2]
A[I]
= A[I+2]
A[I]

## Slide 29: Array Accesses in a loop
  FOR I = 0 to 5
  A[2*I] = A[2*I+1] + 1
0 1 2 3 4 5 6 7 8 9 10 11 12
0 1 2 3 4 5
Iteration Space
Data Space
= A[2*I+1]
A[2*I]
= A[2*I+1]
A[2*I]
= A[2*I+1]
A[2*I]
= A[2*I+1]
A[2*I]
= A[2*I+1]
A[2*I]
= A[2*I+1]
A[2*I]

## Slide 30: Distance Vectors
A loop has a distance d if there exist a data dependence from iteration i to j and d = j-i
  FOR I = 0 to 5
  A[I] = A[0] + 1
  FOR I = 0 to 5
  A[I+1] = A[I] + 1
  FOR I = 0 to 5
  A[I] = A[I+2] + 1
  FOR I = 0 to 5
  A[I] = A[I] + 1

## Slide 31: Multi-Dimensional Dependence
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I, J-1] + 1
J
I

## Slide 32: Multi-Dimensional Dependence
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I, J-1] + 1
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I+1, J] + 1
J
I
J
I

## Slide 33: Outline
Dependence Analysis
Increasing Parallelization Opportunities

## Slide 34: What is the Dependence?
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I-1, J+1] + 1
J
I
0 1 2 3 4 5
0
1
2
3
4

## Slide 35: What is the Dependence?
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I-1, J+1] + 1
J
I
0 1 2 3 4 5
0
1
2
3
4

## Slide 36: What is the Dependence?
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I-1, J+1] + 1
J
I

## Slide 37: What is the Dependence?
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I-1, J+1] + 1
  FOR I = 1 to n
  FOR J = 1 to n
  B[I] = B[I-1] + 1
J
I
J
I

## Slide 38: What is the Dependence?
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I-1, J+1] + 1
  FOR I = 1 to n
  FOR J = 1 to n
  B[I] = B[I-1] + 1
J
I
J
I
  dv=[1, -1]

## Slide 39: What is the Dependence?
  FOR i = 1 to N-1
  FOR j = 1 to N-1
  A[i,j] = A[i,j-1] + A[i-1,j];
J
I

## Slide 40: Recognizing FORALL Loops
Find data dependences in loop
  For every pair of array acceses to the same array
  If the first access has at least one dynamic instance (an iteration) in which it refers to a location in the array that the second access also refers to in at least one of the later dynamic instances (iterations).
  Then there is a data dependence between the statements
  (Note that same array can refer to itself – output dependences)
Definition
  Loop-carried dependence: dependence that crosses a loop boundary
If there are no loop carried dependences  parallelizable

## Slide 41: Data Dependence Analysis
I: Distance Vector method
II: Integer Programming

## Slide 42: Distance Vector Method
The ith loop is parallelizable for all dependence d = [d1,…,di,..dn] either one of d1,…,di-1 is > 0 or all d1,…,di = 0

## Slide 43: Is the Loop Parallelizable?
  FOR I = 0 to 5
  A[I] = A[0] + 1
  FOR I = 0 to 5
  A[I+1] = A[I] + 1
  FOR I = 0 to 5
  A[I] = A[I+2] + 1
  FOR I = 0 to 5
  A[I] = A[I] + 1
Yes
No
No
No

## Slide 44: Are the Loops Parallelizable?
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I, J-1] + 1
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I+1, J] + 1
J
I
J
I
Yes
No
No
Yes

## Slide 45: Are the Loops Parallelizable?
  FOR I = 1 to n
  FOR J = 1 to n
  A[I, J] = A[I-1, J+1] + 1
  FOR I = 1 to n
  FOR J = 1 to n
  B[I] = B[I-1] + 1
J
I
J
I
  dv=[1, -1]
No
Yes
No
Yes

## Slide 46: Integer Programming Method
Example
  FOR I = 0 to 5
  A[I+1] = A[I] + 1
Is there a loop-carried dependence between A[I+1] and A[I]
  Are there two distinct iterations iw and ir such that A[iw+1] is the same location as A[ir]
   integers iw, ir 0 ≤ iw, ir ≤ 5 iw  ir iw+ 1 = ir
Is there a dependence between A[I+1] and A[I+1]
  Are there two distinct iterations i1 and i2 such that A[i1+1] is the same location as A[i2+1]
   integers i1, i2 0 ≤ i1, i2 ≤ 5 i1  i2 i1+ 1 = i2 +1

## Slide 47: Integer Programming Method
Formulation
   an integer vector i̅ such that Â i̅ ≤ b̅ where Â is an integer matrix and b̅ is an integer vector
  FOR I = 0 to 5
  A[I+1] = A[I] + 1

## Slide 48: Iteration Space
N deep loops  n-dimensional discrete cartesian space
Affine loop nest  Iteration space as a set of linear inequalities
  0 ≤ I
  I ≤ 6
  I ≤ J
  J ≤ 7
0 1 2 3 4 5 6 7  J
0
1
2
3
4
5
6
I 
  FOR I = 0 to 5
  A[I+1] = A[I] + 1

## Slide 49: Integer Programming Method
Formulation
   an integer vector i̅ such that Â i̅ ≤ b̅ where Â is an integer matrix and b̅ is an integer vector
Our problem formulation for A[i] and A[i+1]
   integers iw, ir 0 ≤ iw, ir ≤ 5 iw  ir iw+ 1 = ir
  iw  ir is not an affine function
    divide into 2 problems
    Problem 1 with iw < ir and problem 2 with ir < iw
    If either problem has a solution  there exists a dependence
  How about iw+ 1 = ir
    Add two inequalities to single problem iw+ 1 ≤ ir, and ir ≤ iw+ 1
  FOR I = 0 to 5
  A[I+1] = A[I] + 1

## Slide 50: Integer Programming Formulation
Problem 1
  0 ≤ iw
  iw ≤ 5
  0 ≤ ir
  ir ≤ 5
  iw < ir
  iw+ 1 ≤ ir
  ir ≤ iw+ 1
  FOR I = 0 to 5
  A[I+1] = A[I] + 1

## Slide 51: Integer Programming Formulation
Problem 1
  0 ≤ iw  -iw ≤ 0
  iw ≤ 5  iw ≤ 5
  0 ≤ ir  -ir ≤ 0
  ir ≤ 5  ir ≤ 5
  iw < ir  iw - ir ≤ -1
  iw+ 1 ≤ ir  iw - ir ≤ -1
  ir ≤ iw+ 1  -iw + ir ≤ 1
  FOR I = 0 to 5
  A[I+1] = A[I] + 1

## Slide 52: Integer Programming Formulation
Problem 1
  0 ≤ iw  -iw ≤ 0 -1 0 0
  iw ≤ 5  iw ≤ 5 1 0 5
  0 ≤ ir  -ir ≤ 0 0 -1 0
  ir ≤ 5  ir ≤ 5 0 1 5
  iw < ir  iw - ir ≤ -1 1 -1 -1
  iw+ 1 ≤ ir  iw - ir ≤ -1 1 -1 -1
  ir ≤ iw+ 1  -iw + ir ≤ 1 -1 1 1
and problem 2 with ir < iw
Â
b̅

## Slide 53: Generalization
An affine loop nest
  FOR i1 = fl1(c1…ck) to Iu1(c1…ck)
  FOR i2 = fl2(i1,c1…ck) to Iu2(i1,c1…ck)
  ……
  FOR in = fln(i1…in-1,c1…ck) to Iun(i1…in-1,c1…ck)
  A[fa1(i1…in,c1…ck), fa2(i1…in,c1…ck),…,fam(i1…in,c1…ck)]
Solve 2*n problems of the form
    i1 = j1, i2 = j2,…… in-1 = jn-1, in < jn
    i1 = j1, i2 = j2,…… in-1 = jn-1, jn < in
    i1 = j1, i2 = j2,…… in-1 < jn-1
    i1 = j1, i2 = j2,…… jn-1 < in-1
    …………………
    i1 = j1, i2 < j2
    i1 = j1, j2 < i2
    i1 < j1
    j1 < i1

## Slide 54: Outline
Why Parallelism
Parallel Execution
Parallelizing Compilers
Dependence Analysis
Increasing Parallelization Opportunities

## Slide 55: Increasing Parallelization Opportunities
Scalar Privatization
Reduction Recognition
Induction Variable Identification
Array Privatization
Loop Transformations
Granularity of Parallelism
Interprocedural Parallelization

## Slide 56: Scalar Privatization
Example
  FOR i = 1 to n
  X = A[i] * 3;
  B[i] = X;
Is there a loop carried dependence?
What is the type of dependence?

## Slide 57: Privatization
Analysis:
  Any anti- and output- loop-carried dependences
Eliminate by assigning in local context
  FOR i = 1 to n
  integer Xtmp;
  Xtmp = A[i] * 3;
  B[i] = Xtmp;
Eliminate by expanding into an array
  FOR i = 1 to n
  Xtmp[i] = A[i] * 3;
  B[i] = Xtmp[i];

## Slide 58: Privatization
Need a final assignment to maintain the correct value after the loop nest
Eliminate by assigning in local context
  FOR i = 1 to n
  integer Xtmp;
  Xtmp = A[i] * 3;
  B[i] = Xtmp;
  if(i == n) X = Xtmp
Eliminate by expanding into an array
  FOR i = 1 to n
  Xtmp[i] = A[i] * 3;
  B[i] = Xtmp[i];
  X = Xtmp[n];

## Slide 59: Another Example
How about loop-carried true dependences?
Example
  FOR i = 1 to n
  X = X + A[i];
Is this loop parallelizable?

## Slide 60: Reduction Recognition
Reduction Analysis:
  Only associative operations
  The result is never used within the loop
Transformation
  Integer Xtmp[NUMPROC];
  Barrier();
  FOR i = myPid*Iters to MIN((myPid+1)*Iters, n)
  Xtmp[myPid] = Xtmp[myPid] + A[i];
  Barrier();
  If(myPid == 0) {
  FOR p = 0 to NUMPROC-1
  X = X + Xtmp[p];
  …

## Slide 61: Induction Variables
Example
  FOR i = 0 to N
  A[i] = 2^i;
After strength reduction
  t = 1
  FOR i = 0 to N
  A[i] = t;
  t = t*2;
What happened to loop carried dependences?
Need to do opposite of this!
  Perform induction variable analysis
  Rewrite IVs as a function of the loop variable

## Slide 62: Array Privatization
Similar to scalar privatization
However, analysis is more complex
  Array Data Dependence Analysis: Checks if two iterations access the same location
  Array Data Flow Analysis: Checks if two iterations access the same value
Transformations
  Similar to scalar privatization
  Private copy for each processor or expand with an additional dimension

## Slide 63: Loop Transformations
A loop may not be parallel as is
Example
  FOR i = 1 to N-1
  FOR j = 1 to N-1
  A[i,j] = A[i,j-1] + A[i-1,j];
J
I

## Slide 64: Loop Transformations
A loop may not be parallel as is
Example
  FOR i = 1 to N-1
  FOR j = 1 to N-1
  A[i,j] = A[i,j-1] + A[i-1,j];
After loop Skewing
  FOR i = 1 to 2*N-3
  FORPAR j = max(1,i-N+2) to min(i, N-1)
  A[i-j+1,j] = A[i-j+1,j-1] + A[i-j,j];
J
I
J
I

## Slide 65: Granularity of Parallelism
Example
  FOR i = 1 to N-1
  FOR j = 1 to N-1
  A[i,j] = A[i,j] + A[i-1,j];
Gets transformed into
  FOR i = 1 to N-1
  Barrier();
  FOR j = 1+ myPid*Iters to MIN((myPid+1)*Iters, n-1)
  A[i,j] = A[i,j] + A[i-1,j];
  Barrier();
Inner loop parallelism can be expensive
  Startup and teardown overhead of parallel regions
  Lot of synchronization
  Can even lead to slowdowns
J
I

## Slide 66: Granularity of Parallelism
Inner loop parallelism can be expensive
Solutions
  Don’t parallelize if the amount of work within the loop is too small
  or
  Transform into outer-loop parallelism

## Slide 67: Outer Loop Parallelism
Example
  FOR i = 1 to N-1
  FOR j = 1 to N-1
  A[i,j] = A[i,j] + A[i-1,j];
After Loop Transpose
  FOR j = 1 to N-1
  FOR i = 1 to N-1
  A[i,j] = A[i,j] + A[i-1,j];
Get mapped into
  Barrier();
  FOR j = 1+ myPid*Iters to MIN((myPid+1)*Iters, n-1)
  FOR i = 1 to N-1
  A[i,j] = A[i,j] + A[i-1,j];
  Barrier();
J
I
I
J

## Slide 68: Unimodular Transformations
Interchange, reverse and skew
Use a matrix transformation Inew = A Iold
Interchange
Reverse
Skew

## Slide 69: Legality of Transformations
Unimodular transformation with matrix A is valid iff. For all dependence vectors v the first non-zero in Av is positive
Example
  FOR i = 1 to N-1
  FOR j = 1 to N-1
  A[i,j] = A[i,j] + A[i-1,j];
Interchange
Reverse
Skew




## Slide 70: Interprocedural Parallelization
Function calls will make a loop unparallelizatble
  Reduction of available parallelism
  A lot of inner-loop parallelism
Solutions
  Interprocedural Analysis
  Inlining

## Slide 71: Interprocedural Parallelization
Issues
  Same function reused many times
  Analyze a function on each trace  Possibly exponential
  Analyze a function once  unrealizable path problem
Interprocedural Analysis
  Need to update all the analysis
  Complex analysis
  Can be expensive
Inlining
  Works with existing analysis
  Large code bloat  can be very expensive

## Slide 72
HashSet h;
for i = 1 to n
  int v = compute(i);
  h.insert(i);
  Are iterations independent?
  Can you still execute the loop in parallel?
  Do all parallel executions give same result?

## Slide 73: Summary
Multicores are here
  Need parallelism to keep the performance gains
  Programmer defined or compiler extracted parallelism
Automatic parallelization of loops with arrays
  Requires Data Dependence Analysis
  Iteration space & data space abstraction
  An integer programming problem
Many optimizations that’ll increase parallelism